Modbus Master configuration File (drvConf.yml)

method – This field tells us which variant of the modbus protocol is being used. (Most common variants are Modbus RTU and Modbus TCP/IP)

port – This feild has the hardware serial port through which the modbus network’s physical layer connects to the master/polling device.

baudrate – Contatins the baudrate being used for the serial communication(UART configuration).

Parity - Contains the type of parity check being used for the serial communication(UART configuration).

timeout – Contains the time in seconds that the master would wait for before executing the timeout condition for the query which didn’t receive a response.

stopbits – Contains the number of stop bits used for the serial communication(UART configuration).

bytesize – Contains the number of data bits per frame(character length) used for serial communication(UART configuration).

MAX_POLL_RATE - Contains the maximum number of polls that the master is capable of per second.

Modbus Slave configuration File (conf.d/sensorConf.yml)

name – This field contains the name of the sensor/actuator. The feild must be a string.

location – This field contains the description of the physical location of the sensor. The field must be a string.

state – This field defines the current state of the modbus device
The field must be a string and can only be active, inactive or dormant. When set to active, the master polls the device. When set to inactive, the master does not poll this device. When the state is dormant, it means that the device is waiting to be discovered and assigned the modbus device ID(modbusDevID).

priority – This field defines the priority of the device. This is used to decide which devices can be dropped in case the maximum polling rate condition is reached. The field must be an integer in the range – [0, 2] where 0 has highest priority.

readRegs – This field contains information about the registers to be polled by the master. The field is a list of dictionaries. The dictionary contains the following fields:

addr – Contains the address of the register. The field must be an integer.
nRegs – Contains the number of contiguous 16-bit registers to be polled for. The field must be an integer and it can be at max 100.
unit – This field is a string and contains the name of the unit in which the sensor data is stored in the register.
rate – This field contains an integer that stores the number of times the register needs to be polled per second.
mqttTopic – This filed is a string and it contains the MQTT topic to which the received data is to be published.

The size of the list would be the number of non-contiguous blocks to be polled for.

writeRegs – This field is contains information about the registers that need to be written by the master. The field is a list of dictionaries. The dictionary contains the following fields:

addr – Contains the address of the register. The field must be an integer.
mqttTopic – This filed is a string and it contains the MQTT topic from which the data to be written is extracted.
rate – This field contains an integer that stores the number of times the register needs to be written per second.

The size of the list would be the number of non-contiguous blocks to be polled for.